## Slide 1
Front end team …..
ADI/CU GP 2025/2026
Progress Update Meeting (1)
Part (1) : FFT task

## Slide 2: Meeting Timeline
Parallelization Techniques
Sarah
Ali
HWPE
Sama
Mohamed Abdel-hay
HW/SW (Co-Design)
Mostafa Ahmed
Mostafa Yousry
FFT
Marwan
Mostafa Fathy
0
01
02
03
04
Presentation part (1) : FFT task
Presentation part (2) : HWPE
Presentation part (3) : Parallelization Techniques

## Slide 3: Agenda
Introduction
Modeling
RTL
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)

## Slide 4: Introduction

## Slide 5: Agenda
Introduction
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 6: Introduction :DFT Definition
DFT: it stands for Discrete Fourier Transform which is the tool to transform the discrete signal in time domain to discrete in frequency domain
Time domain signal
DFT
Frequency domain signal
Mathematical model :
Where : X[k] is the input signal in frequency domain
x[n] is the input signal in time domain
which =
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 7: Introduction :DFT calculation methods
DFT
Direct computation
FFT
Sum
Matrix form
1- Sum
Computation Methodology:
Using nested for loop one for K and one for N
Complexity :
Direct computation:
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 8: Introduction :DFT calculation methods
DFT
Direct computation
FFT
Sum
Matrix form
2- Matrix form
Computation Methodology:
Matrix multiplication
Complexity :
1- Sum
Computation Methodology:
Using nested for loop one for K and one for N
Complexity :
Direct computation:
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 9: Introduction :FFT
DFT
Direct computation
FFT
Sum
Matrix form
FFT: The Fast Fourier Transform (FFT) is an algorithm that computes the Discrete Fourier Transform (DFT) of a sequence
Algorithm categories :
Cooley-Tukey algorithm
Radix -2
Radix -4
Decimation in frequency (DIF)
Decimation in time
(DIT)
Radix -2
Radix -4
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 10: Introduction :FFT
Complexity table of DFT computation :
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 11: Introduction :FFT
Complexity table of DFT computation :
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4
x(0)
x(1)
X(0)
X(1)
2-point DFT
Show Equation
Substitute with W
x(0)
x(1)
X(0)
4-point DFT
Show Equation
Substitute with W
x(2)
x(3)
X(1)
X(2)
X(3)

## Slide 12: Introduction :FFT
8-point DFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4
64 Multiplication (16 complex)

## Slide 13: Introduction :FFT
Mathematical Perspective :starting for DFT formal definition
After some mathematical manipulation we could prove that
Where :
b
So, are they exactly equivalent ?
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 14: Introduction :FFT
8-point DFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
a(0)
a(1)
a(2)
a(3)
b(4)
b(5)
b(6)
b(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
Splitter
Why do we call it “Splitter” ?
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 15: Introduction :FFT
4-point FFT
a(0)
a(1)
a(2)
a(3)
b(4)
b(5)
b(6)
b(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
Splitter
1 Problem
8-point
2 independent Problems
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 16: Introduction :FFT
So, we could generalize it to be :
N-point FFT
- point FFT
Splitter
- point FFT
So , when should we stop ?
It depends on the radix . Since we are working with radix-2 , we should stop at 2-point calculation
8 points
4 points
4 points
2 points
2 points
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 17: Introduction :FFT
8 points
Splitter
4-point
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 18: Introduction :FFT
4 points
Splitter
4-point
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 19: Introduction :FFT
4 points
Splitter
4-point
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 20: Introduction :FFT
8 points
Splitter
4-point
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 21: Introduction :FFT
8 points
Splitter
4 points
4 points
Splitter
2 points
2 points
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 22: Introduction :FFT
8 points
4 points
4 points
Splitter
2 points
2 points
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 23: Introduction :FFT
8 points
Splitter
Splitter
Splitter
2 points
2 points
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 24: Introduction :FFT
Complexity calculation :
Because we are continuously dividing by 2, we can determine the exact number of operations based on two factors:
Number of Stages: Since we divide the sequence in half at each step until we reach 2 points
the total number of stages is equal to
  multiplication per Stage: In every stage, we do
The Final Complexity Formulas :
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 25: Introduction :Direct computation vs FFT
Code Flow
Generate bits
Call FFT
Call DFT
Comparing the performance
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 26: Introduction :Direct computation vs FFT
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 27: Introduction :Direct computation vs FFT
Execution Time
4096 point
32768 point
16384 point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 28: Introduction :Radix-2 vs Radix-4
Number of stages:
Radix-2:
Radix-4:
So, Radix-4 has fewer stages, but does that mean it is better?
Software Perspective: The real bottleneck is memory access. The savings come from reducing the number of times the processor has to write intermediate data to the RAM and read it back again. By cutting the stages from
down to Radix-4 cuts the most expensive operation in software (cache/RAM access) exactly in half.
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 29: Introduction :Radix-2 vs Radix-4
Hardware perspective :
The real bottleneck is the stage component
In a pipelined FFT architecture, Radix-2 outperforms Radix-4 in maximum frequency because it has a simpler critical path
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4
Radix-2 SDF: Shorter critical path → Higher ​ → Higher maximum throughput.
Radix-4 SDF: Longer critical path but ≈50% fewer complex multipliers → Better Area/Power efficiency

## Slide 30: Agenda
System definition
Modeling
RTL
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)

## Slide 31: Modeling

## Slide 32: Agenda
Modeling
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 33: Modeling :System Modeling
Mapper
N-point IFFT
Adding cyclic extension
Input data
To the channel
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
Equalizer
De-mapper
De-mapper
Multiplexer
from the channel
from the channel
Output data
Tx (UE)
Rx (Base Station)
  Challenges
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 34: Modeling :Algorithm and Architecture
Algorithm: we implemented the Cooley-Tukey algorithm (Radix-2, DIF)
Architecture :we implemented the SDF architecture (Radix-2, DIF)
Why SDF ?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 35: Recall: Rx block diagram
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
Equalizer
De-mapper
De-mapper
De-mapper
Multiplexer
from the channel
from the channel
from the channel
Output data
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 36: FFT Modeling :Algorithm and Architecture
Algorithm: we implemented the Cooley-Tukey algorithm (Radix-2, DIF)
Architecture :we implemented the SDF architecture (Radix-2, DIF)
Why SDF ?
Pros:
Area Efficiency.
Area scaling
Cons:
higher latency (N-1)
low throughput (1 sample/cycle)
High power density
Given the high number of parallel streams in the base station, we prioritized minimizing the area per block over maximizing the single-stream throughput.
But would it really be enough for the required data rate ?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 37: Recall: System Configuration
signal BW, sampling rate
Bandwidth (MHz) | NFFT | NusedFFT (Subcarriers) | NumRBs | Sampling Rate (MHz)
50 | 512 | 384 | 32 | 61.44
100 | 1024 | 792 | 66 | 122.88
400 | 4096 | 3168 | 264 | 491.52
Note: these calculation based on Subcarrier Spacing (SCS): 120 kHz
Would it support 491.52 MHz?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 38: FFT Modeling :Algorithm and Architecture
Platform constraints: "Baseline Frequency: 500 MHz (Validated by a silicon-proven 40nm tape-out)." [1]
Critical Path
So , What is the for the target technology?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 39: Recall :Adflow Metrics Summary for 3 stages
Metric | Value
Maximum clock frequency | 619.5 MHz
WNS (setup) | 3.386 ns
TNS (setup) | 0
WNS (hold) | 0
TNS (hold) | 0
Post-route utilization | 59.7 %
Technology | GF 22nm
Standard Cell Library | 22nm_gf_fdx_10m
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 40: Modeling:SDF Block Diagram
SDF DIF radix-2
12 bits input
S1
S2
S12
12 bits output
2
2
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 41: Modeling: Fixed point analysis
Q1.11
Q3.9
Q4.8
Q4.8
Q5.7
Q6.6
Q6.6
Q7.5
Q7.5
Q8.4
Q8.4
Q9.3
Q9.3
Stage1
Stage2
Stage3
Stage4
Stage5
Stage6
Stage7
Stage8
Stage9
Stage10
Stage11
Stage12
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 42: Modeling: Fixed point analysis
Q1.11
Q3.9
Q4.8
Q4.8
Q5.7
Q6.6
Q6.6
Q7.5
Q7.5
Q8.4
Q8.4
Q9.3
Q9.3
Stage1
Stage2
Stage3
Stage4
Stage5
Stage6
Stage7
Stage8
Stage9
Stage10
Stage11
Stage12
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
Chart: Fixed Point Analysis
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Expected truncation | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | -1
MATLAB FxPt | 11 | 9 | 8 | 8 | 7 | 6 | 6 | 5 | 5 | 4 | 4 | 3 | 3

## Slide 43: Modeling : SQNR analysis
Example FFT Output Comparison:
Bin | Reference | Fixed point | Error (Magnitude)
1 | −25.92 −16.64i | −25.75 −16.50i | 0.2202
2 | −42.93 −59.19i | −43.00 −59.25i | 0.0922
3 | 8.23 −31.22i | 8.25 −31.13i | 0.0922
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 44: Modeling : SQNR analysis
 | FlPt | FxPt
SQNR |  | 
Mean Error |  | 
Average SQNR = 227.02 dB
Average SQNR = 48.35 dB
Avg Mean error : 1.59 ×
Avg Mean error: 2.417 ×
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 45: Modeling : Challenges
SQNR optimization
Recall : General block diagram
SDF DIF radix-2
12 bits input
S1
S2
S12
12 bits output
2
2
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 46: Modeling : Challenges
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
SDF DIF radix-2
S1
S2
S12
2
2
12 bits input
12 bits output

## Slide 47: Modeling : Challenges
Level 1 (Floor rounding – No delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
Could we do better ?
41.25 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 48: Modeling : Challenges
Level 2 (Floor rounding – No delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Recall :
Output equations :
b
Datapath Optimization: Delaying truncation until after the twiddle factor multiplication to improve SQNR
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 49: Modeling : Challenges
Level 2 (Floor rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
Small change , but can we take the SQNR to the next level ?
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 50: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
RoundingMethod:
OverflowAction:
1-Saturate
2-Wrap
Fimath (Fixed-point Mathematic object)
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
1-Floor
2-Celling
3-Zero
4-Nearest
5-Round
6-Convergent

## Slide 51: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
RoundingMethod:
Fimath (Fixed-point Mathematic object)
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
1-Floor
2-Celling
3-Zero
4-Nearest
5-Round
6-Convergent
Advantages:
Eliminates rounding bias
Prevents error accumulation across stages
Improves SQNR performance
Matches RTL hardware implementation
Industry standard in DSP hardware

## Slide 52: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
Level 3
Convergent rounding
delayed quantization
Bit truncation
48.35 dB
0.75 dB
6.45 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 53: Agenda
System definition
Modeling
RTL
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)

## Slide 54: RTL

## Slide 55: Agenda
RTL
  SDF Block diagram
  Stage Block diagram
  Stage main component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 56: RTL : stage block diagram
Let's focus on the architecture of a single stage
SDF DIF radix-2
12 bits input
R2
R2
R2
12 bits output
2
2
SDF DIF radix-2
12 bits input
R2
R2
R2
12 bits output
2
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 57: RTL : stage block diagram
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
Output equations :
b

## Slide 58: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
1- Butterfly Function: the core of the stage it does both addition and subtraction, and, in some implementation, it contains also the multiplier block
2- Multiplier Function: Multiplication the output difference from the Butterfly unit

## Slide 59: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
3- Output multiplexer Function: It is used to route the difference (output of the FIFO) and summation to the output (the next stage)
4- Bypass multiplexer Function: It is used to Bypass the summation without multiplying it by the twiddle factors
5- Twiddle factor ROM Function: It holds the values of twiddle factors
0
1
Mux
Twiddle factor ROM

## Slide 60: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
6- FIFO: Function: It’s used to store the input and the difference from the Butterfly unit
7- FIFO multiplexer Function: It’s used to route the input and the output difference to the FIFO
12 bits input
2
0
1
Mux

## Slide 61: RTL: FSM
For demonstration purposes, we will use an 8-point FFT (N=8) , while each stage has its own FSM we will work on stage (1) so the size of FIFO=N/2=4
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
12 bits input
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 62: RTL: FSM
The first state is the IDLE state. The system remains inactive until the wake-up signal
(valid_in) is asserted. This signal is generated by external logic
alongside the input data this is for stage (1) but for the other stages it comes
From the (valid_out) of the previous stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x0
x1
x2
x3
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 63: RTL: FSM
After waking up, the finite state machine (FSM) transitions to the Fill state.
As the name implies, during this state,
the first half of the input samples are loaded into the FIFO.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x0
x1
x2
x3
x4
x5
x6
x7
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 64: RTL: FSM
In the Butterfly state, the second half of the input arrives and bypasses the FIFO. Instead, it is processed directly with the first half that we stored earlier. Regarding the outputs of the Butterfly unit: the sum goes directly to the next stage through the output MUX, while the difference is loaded back into the FIFO for the next cycle It is also important to note that once the first output is available, the valid_out signal is asserted to notify the subsequent stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
valid_out
x0
x1
x2
x3
x4
x5
x6
x7
S0
D0
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 65: RTL: FSM
In the Butterfly state, the second half of the input arrives and bypasses the FIFO. Instead, it is processed directly with the first half that we stored earlier. Regarding the outputs of the Butterfly unit: the sum goes directly to the next stage through the output MUX, while the difference is loaded back into the FIFO for the next cycle It is also important to note that once the first output is available, the valid_out signal is asserted to notify the subsequent stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
D0 D1 D2 D3
2
S0
S1
S2
S3
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x7 x6 x5 x4
x3 x2 x1 x0
valid_out
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 66: RTL: FSM
Finally, we reach the Drain state. Here, we perform two operations concurrently. The stored difference data is multiplied by the appropriate twiddle factor and then routed to the next stage. Simultaneously, we load the incoming data for the next frame directly into the FIFO to keep the pipeline completely full.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
valid_out
D3
D2
D1
D0
x0
x1
x2
x3
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 67: RTL: FSM
Finally, we reach the Drain state. Here, we perform two operations concurrently. The stored difference data is multiplied by the appropriate twiddle factor and then routed to the next stage. Simultaneously, we load the incoming data for the next frame directly into the FIFO to keep the pipeline completely full.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
x0 x1 x2 x3
2
D0
D1
D2
D3
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
D0 D1 D2 D3
valid_out
x4
x5
x6
x7
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 68: RTL: FSM
From this point, the FSM simply alternates between the Butterfly and Drain states to continuously process the incoming data. This loop continues as long as data is flowing. Once the valid_in signal is De-asserted , meaning we have reached the end of the packet , the FSM transitions back to the IDLE state, ready for the next frame.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 69: RTL: Simulation results and latency calculation
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Verification Results for 100 Frames
Latency calculation check == (N-1 )
Latency=

## Slide 70: RTL: Challenges
Rounding vs truncation (flooring )
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits input
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
Convergent Rounding

## Slide 71: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Convergent Rounding
(rounding to the nearest even number)
13-bit input
12-bit output
Ex:
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
13-bit input
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
As we can see we didn’t round the LSB (0) as it’s even but what if the LSB was 1 ? Let’s see
12-bit output

## Slide 72: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Ex:
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1
13-bit input
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
We rounded it up, so it became even and to understand the logic let’s call the bit (1) in the input L and the bit (0) S then we have rounded bit Which= L & S and then we take this rounded bit and add it to the input [12:1]
let’s revisit the last example again
12-bit output
L=1 , S=1 -> rounded bit =1 , output= input [12:1] + rounded bit = [000000001101]+[1’b1] =[000000001110]
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1
13-bit input
S
L

## Slide 73: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Let’s compare Convergent Rounding to other two rounding methods (Round-floor )
Recall :
Rounding Methods :
1-Floor
2-Celling
3-Zero
4-Nearest
5-Round
6-Convergent

## Slide 74: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Why does the convergent rounding enhance the SQNR by 6 dB compared to floor rounding ?
This is because Floor rounding consistently rounds down, introducing a DC offset that degrades the SQNR
 | Floor | Convergent rounding
SQNR |  | 
Average SQNR = 41.9 dB
Average SQNR = 48.35 dB

## Slide 75: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Why does Convergent Rounding enhance the SQNR by ~2 dB compared to Standard Rounding (Round) ?
Standard Rounding Issue: It rounds up for positive signals and down for negative signals. While this doesn't introduce a DC offset, it makes the quantization error dependent on the signal itself. This correlation creates unwanted harmonics.
The Convergent Advantage: It breaks ties based on the Least Significant Bit (LSB). Since the LSB acts as a random variable, it decorrelates the error from the signal, turning the error into evenly distributed "white noise."
Proof in Frequency Domain: Let’s look at the next demo lab result. We input a single-tone signal and monitored the error spectrum for both methods to see this difference clearly

## Slide 76: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
 | Time domain | Frequency domain
Round |  | 
Convergent Rounding |  | 

## Slide 77: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
As seen in the previous figure, when the error is dependent on the signal, it introduces severe distortion in the frequency domain. In contrast, with Convergent Rounding, the error becomes like noise spread evenly across all frequencies
Note: Rounding and Convergent Rounding behave identically for any value not exactly at 0.5 (e.g., both round 3.4 to 3, and 3.6 to 4). Their behavior only diverges at exact half-way points (e.g., 3.5) due to their different tie-breaking rules
Example: Q11.1 to Q12.0 Conversion Let's assume the input value is 2.5. We need to remove the 1 fractional bit to get an integer output (Q12.0).
Convergent Rounding: Rounds to the nearest even number → 2
Standard Round: Rounds up (away from zero) → 3
Floor (Truncation): Rounds down → 2
Final Note: Round and Convergent Rounding outperform Floor not only by preventing severe DC offset, but also by minimizing the maximum quantization error. They introduce a worst-case error of 0.5 LSB, whereas Floor introduces an error approaching 1 LSB

## Slide 78: RTL: Challenges
Convergent Rounding
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
 | Convergent Rounding | Floor | Round
DC offset | No | Yes | No
Maximum Quantization error | 0.5 bit | 1 bit | 0.5 bit
SQNR values | 48.35 dB | 41.9 dB | 46.4dB

## Slide 79: RTL: Challenges
Different Q notation form sum and multiplier
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
FIFO
Q2.10
Q2.10
Q3.9
Q3.9
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 80: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Bit reversal :
Recall :
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(4)
X(2)
X(6)
X(1)
X(5)
X(3)
X(7)
Scrambled Output
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ordered Output

## Slide 81: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(4)

## Slide 82: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
Ordered Output
X^(0)
X^(4)

## Slide 83: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
Ordered Output
X^(0)
Memory (B)
X^(4)

## Slide 84: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
Memory (A)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
4-Switch the roles: Now Memory A receives the data while Memory B outputs it
Ordered Output
Memory (B)
X^(4)
X^(1)
X^(2)
X^(3)
X^(5)
X^(6)
X^(6)
X^(0)

## Slide 85: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
Memory (A)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
4-Switch the roles: Now Memory A receives the data while Memory B outputs it
X^(0)
z
Memory (B)
X^(4)
X^(1)
X^(2)
X^(3)
X^(5)
X^(6)
X^(6)
Ordered Output

## Slide 86: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Bit reversal :
Problems :
Increasing the area (12.5 KB RAM )
Reducing the max frequency and increasing the power consumption
Increasing the latency form (N-1 ) to (2N-1)
Could we optimize the DIF scrambled output on the system level ?
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
Equalizer
De-mapper
De-mapper
Multiplexer
from the channel
from the channel
Output data
Rx (Base Station)

## Slide 87: RTL: Final Architecture
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
fft4096_dif
in_r
in_i
out_r
out_i
valid_out
Frame_done
out_index
valid_in
rst_n
clk
Singal Name | Function
in_r (input ) , in_r (input) | Input real and input imaginary
valid_in | Asserted when there is a valid input and Enable the FFT block
valid_out | Asserted when there is a valid output
out_r , out_i | output real and output imaginary
Frame done | Asserted when a frame ends ( for one pulse only )
out_index | The index of the current output
parameter (DATA_WIDTH) | The width of data input and output ports
parameter (ORDERED_OUTPUT) | (1) Ordered output , (0) Scrambled output

## Slide 88: RTL: Final Architecture
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
fft4096_dif
ORDERED_OUTPUT
(1) Ordered output
(0) Scrambled output
Ping-Pong
memory architecture
Scrambled Output
Ordered Output

## Slide 89: Agenda
System definition
Modeling
RTL
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)

## Slide 90: HW/SW Co-design (HW Part)

## Slide 91: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification (1)
  Optimizations
  Software & Verification (2)

## Slide 92: HW/SW Co-design : Problem Statement
Objective:
  Integrate a custom-designed Radix-2 FFT Butterfly hardware accelerator into the PULP platform as an AXI peripheral and drive it with a complete software FFT implementation.
Goal:
  Validate correct hardware/software interaction.
Scope of current work:
  Hardware Scope:
    RTL of radix-2 Butterfly, Map the standalone butterfly accelerator to the AXI bus, design the protocol translation wrapper, and a simple Software validation using a simple C test.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 93: HW/SW Co-design : Butterfly Operation
Core Function:
  The accelerator executes the Radix-2 Decimation-in-Frequency (DIF) butterfly, the fundamental arithmetic building block of the FFT algorithm.
Mathematical Formulation:
Where: L,R : Complex input samples , W : Twiddle factor
Functional Role in FFT:
  Combines input samples
  Applies twiddle rotation
  Produces intermediate FFT outputs
Hardware Role:
  By offloading this highly repetitive equation to custom silicon, we relieve the processor from complex arithmetic computations.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 94: HW/SW Co-design : RTL Design
Core blocks:
  Add/Subtract Units
  Karatsuba Multiplier
  Pipeline / Delay Alignment
Supporting Modules Originally:
  bimpy
    Base signed multiplier
  Longbimpy
    Extended precision multiplier
    Supports larger operand widths
  convround
    Convergent rounding
Currently Used
  standard multiplication logic
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 95: HW/SW Co-design : Arithmetic Optimization
The Hardware Challenge:
  Complex multiplication is the most expensive operation in our entire Datapath.
  A standard complex multiply requires 4 real multipliers.
The Optimization : Karatsuba Algorithm
  Reformulated the multiplication logic. we complete the math using only 3 real multipliers.
Benefits:
  Reduced multiplier count
  Lower hardware area and power
The Price:
  This approach requires adding extra Adders.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 96: HW/SW Co-design : Pipeline Alignment
Motivation:
  Multiplier introduces computation latency
  Addition path is faster
  Outputs must remain time-aligned
Implemented Solution:
  Auxiliary Signal Propagation
Result:
  The faster mathematical path is delayed to match the slower paths, ensuring the Sum and Difference outputs are aligned.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 97: HW/SW Co-design : PULP Intergation
Objective:
  Expose the butterfly accelerator as a memory-mapped AXI peripheral within the PULP SoC.
Pulp Architecture Overview
The TCDM:
  Normal processors rely on invisible memory caches, which cause unpredictable delays.
  PULP replaces caches with a Tightly Coupled Data Memory (TCDM)—a shared, ultra-fast scratchpad where Software must explicitly place data into the TCDM.
The System Actors:
    Fabric Controller
    Micro-DMA
    Accelerators
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 98: HW/SW Co-design :Highway System – Interconnects and Arbitration
Two Separate Traffic Networks:
  TCDM Interconnect: reserved for fast operations, 1-cycle memory lookups.
  AXI Crossbar: Built for complex components that needs multiple cycles.
How Software Talks to Hardware:
  Address-Based Routing: Hardware doesn't have a name, only a memory address.
Two Paths of Communication:
  The Control Path :The FC configures the hardware by writing values to these addresses.
  The Data Path: Pushing the heavy payloads to the hardware so it can begin computation.
Wrapper
Accelerator
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  Software & Verification
  Arithmetic Optimization
  SOC-Interconnect

## Slide 99: HW/SW Co-design : The Translation Wrapper
The Problem: AXI is Too Complex
  Our custom accelerator doesn't know how to speak the complex AXI handshaking protocol.
Solution
  Translate bus transactions into register-level control via wrapper
The Blueprint (The .hjson file)
  A "contract" between software and hardware.
The Protocol Downgrade :
  AXI  Protocol Converter  REG_BUS
  REG_BUS  Macros  Structs
The Hardware Reality (.q , .qe, .d, .de) :
  The auto-generated register file unpacks those Structs into raw electrical wires:
    .q : Stable Data, .qe: The Spark (1-cycle trigger pulse)
    .d : The Results from the hardware , .de : Data Enable.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 100: HW/SW Co-design : Soc Modifications
Key Modifications:
  Instantiated the top-level wrapper inside the pulp_soc.sv.
  Added a dedicated AXI slave port to the system crossbar.
  Extended the AXI interconnect routing logic to accommodate the new peripheral.
  Updated the global SoC address map to recognize the accelerator.
Address Allocation:
  Assigned a dedicated memory-mapped region for the Butterfly IP.
Result:
  The custom accelerator is now a fully visible, permanently integrated node on the system bus. It is accessible through standard AXI memory transactions.
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 101: HW/SW Co-design : Software & Verification (1)
Step 1: Verify Integration &Mathematical Correctness
  Results Match the results from the Written Testbench
Software Control:
  Simple Custom C test application developed
Execution Flow:
  Write inputs to registers
  Trigger accelerator
  Poll DONE status
  Read computed outputs
Observed Results:
  Correct butterfly arithmetic
  Successful HW/SW communication
Measured Latency For Original butterfly was 442 cycle!!
  Problem Statement
  Butterfly Operation
  RTL Design
  Pipeline Alignment
  PULP integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Arithmetic Optimization

## Slide 102: HW/SW Co-design : Optimization 1 – The Auto-Trigger
The Traditional Approach (3 Bus Transactions):
  Software writes the Left Operand.
  Software writes the Right Operand.
  Software writes a '1' to a CTRL register to wake up the hardware.
Optimized Solution (2 Bus Transactions):
  Eliminated the dedicated "Start" register.
  Flagged the Right Operand register to generate a Write-Enable pulse.
The Benefit:
  The hardware instantly fires up instantly.
  Saves AXI transaction on every single butterfly
Result:
  Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 103: HW/SW Co-design : Optimization 2 – Auto-Status
The Polling Problem:
  Software must manually clear this STATUS flag before new calculation, wasting an AXI transaction.
Solution (The .de Wire):
  status.d = w_o_aux ? 1'b1 : 1’b0, status.de = w_o_aux | op_right.qe
Result:
  Saved another AXI transaction. So,Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 104: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling
Design Feature | Phase 1 (Pipelined) | Phase 2 (Pipelined) | Phase 3 (Pipelined) | Phase 4 (Flattened)
Operand Widths | Oversized: 34b In, 38b Out, 42b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Delivery | Full payload passed over AXI | Full payload passed over AXI | Twiddle Index passed over AXI | Twiddle Index passed over AXI
Wrapper | No optimizations | No optimizations | optimized | optimized
Multiplier Type | Pipelined | Pipelined | Standard | Standard
Software Driver | High Overhead | Optimized | Optimized | Optimized
Latency | 442 cycles | 59 cycles | 24 cycles | 24 cycles

## Slide 105: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling
  Phase 2: Result
  Phase 3: Result

## Slide 106: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling
  Phase 4: Result
  Testbench result

## Slide 107: HW/SW Co-design :Questions
Overhead Sources ?
Pulp-runtime vs SDK, Is there a difference for SW latency and total overhead ?
Are the Results Valid and Logical ?

## Slide 108: Agenda
System definition
Modeling
RTL
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)

## Slide 109: HW/SW Co-design (SW Part)

## Slide 110: Agenda
HW/SW Co-design (SW Part)
  Problem Statement
  Architecture Challenges
  SW vs. HW Data Flow
  Benchmarking Results
  Moving to High-Radix

## Slide 111: Problem Statement
Objective:
Integrate a custom-designed Radix-2 FFT Butterfly hardware accelerator into the PULP platform.
Minimize processing latency
Goal:
Identify and mitigate architectural bottlenecks to surpass the performance of optimized CPU SIMD.
Current limitation:
Communication overhead (AXI bus latency) currently outweighs the speedup gained from hardware arithmetic.

## Slide 112: Architecture Challenges
Time saved by high-speed hardware arithmetic is currently outweighed by the latency of moving operands and results across the AXI.
Cores residing in the Cluster must transition through the Cluster Bus and across the SoC’s Logarithmic Interconnect to reach the AXI bridge.
While the cluster provides eight parallel cores, the SoC AXI bridge acts as a bottleneck, allowing only one transaction to the accelerator at a time

## Slide 113: SW vs. HW Data Flow
Pure Software:
HW/SW:
Load data
Vector
Operations
Write data
Load data
pack 1st op
pack 2nd op
Calc. Tw. IDX
Push 1st op to AXI
Push 2nd op to AXI
HW Operations
Store data
Pull 2nd
result
Pull 1st result
Load data
Write data

## Slide 114: Benchmarking Results
HW/SW:
Pure SW (Single core):
Pure SW (Multiple core):
Butterfly SW:

## Slide 115: Benchmarking Results
Vector Extensions: The software implementation is not standard C code; it heavily utilizes OpenPULP's vector instructions.
AXI and Bit manipulation Overhead: While the hardware executes the actual butterfly arithmetic in a few clock cycles, the CPU spend roughly 50 cycles per butterfly executing bit-shifting operations and waiting for AXI bus.

## Slide 116: Moving to High-Radix
Number of butterfly operations:
Overhead increases linearly:
Speed-up:

## Slide 117: GitHub Repositories
1- MATLAB modeling code for SDF DIF : (Modeling part by Mostafa Fathy)
https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/System-Modelling/SDF-Radix2-FFT
2- SDF 4092-point code : (RTL part by Marwan Khaled and Mostafa Fathy)
https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/RTL/FFT_SDF
3- Source code can be found here: (Firmware part by Mostafa Yossry) https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/Firmware/Radix2-FFT 4- RTL implementations and Wrapper codes can be found here: (AXI integration part by Mostafa Ahmed)
https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/RTL/simple_butterfly/simple_butterfly

## Slide 118: References
Mr.Wolf: An Energy-Precision Scalable Parallel Ultra Low Power SoC for IoT Edge Processing:
https://pulp-platform.org/docs/publications/08715500.pdf [1]
Fast Fourier Transform :Algorithms And Applications)
https://danylastchild07.wordpress.com/wp-content/uploads/2016/05/fft_algorithms-and-applications.pdf
VLSI Digital Signal Processing Systems: Design and Implementation
https://d1.amobbs.com/bbs_upload782111/files_18/ourdev_480582.pdf
PULP platform
https://pulp-platform.org/index.html

## Slide 119
Thank You!