## Slide 1
Front end team …..
ADI/CU GP 2025/2026
Progress Update Meeting (1)
Part (1) : FFT task

## Slide 2: Agenda
Introduction
Modeling
RTL
Firmware
HW/SW Co-design

## Slide 3: Introduction

## Slide 4: Agenda
Introduction
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 5: Introduction :DFT Definition
DFT: it stands for Discrete Fourier Transform which is the tool to transform the discrete signal in time domain to discrete in frequency domain
Time domain signal
DFT
Frequency domain signal
Mathematical model :
Where : X[k] is the input signal in frequency domain
x[n] is the input signal in time domain
which =
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 6: Introduction :DFT calculation method
DFT
Direct computation
FFT
Sum
Matrix form
1- Sum
Computation Methodology:
Using nested for loop one for K and one for N
Complexity :
Direct computation:
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 7: Introduction :DFT calculation method
DFT
Direct computation
FFT
Sum
Matrix form
2- Matrix form
Computation Methodology:
Matrix multiplication
Complexity :
1- Sum
Computation Methodology:
Using nested for loop one for K and one for N
Complexity :
Direct computation:
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 8: Introduction :FFT
DFT
Direct computation
FFT
Sum
Matrix form
FFT: The Fast Fourier Transform (FFT) is an algorithm that computes the Discrete Fourier Transform (DFT) of a sequence
Algorithm categories :
Cooley-Tukey algorithm
Radix -2
Radix -4
Decimation in frequency (DIF)
Decimation in time
(DIT)
Radix -2
Radix -4
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 9: Introduction :FFT
Complexity table of DFT computation :
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
Number of points | Number of multiplication
2 | 4
4 | 16
8 | 64
… | ….
1024 | 
Question : could we replace an 8-point calculation with two 4-point calculations ?
If so , we could reduce the number of multiplications from 64 to just 32
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 10: Introduction :FFT
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 11: Introduction :FFT
Mathematical Perspective :starting for DFT formal definition
After some mathematical manipulation we could prove that
Where :
b
So, are they exactly equivalent ?
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 12: Introduction :FFT
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
a(0)
a(1)
a(2)
a(3)
b(4)
b(5)
b(6)
b(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
Splitter
Why do we call it “Splitter” ?
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 13: Introduction :FFT
4-point FFT
a(0)
a(1)
a(2)
a(3)
b(4)
b(5)
b(6)
b(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
4-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
Splitter
1 Problem
8-point
2 independent Problems
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 14: Introduction :FFT
So, we could generalize it to be :
N-point FFT
- point FFT
Splitter
- point FFT
So , when should we stop ?
It depends on the radix . Since we are working with radix-2 , we should stop at 2-point calculation
8 points
4 points
4 points
2 points
2 points
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 15: Introduction :FFT
8 points
Splitter
4-point
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 16: Introduction :FFT
4 points
Splitter
4-point
4-point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 17: Introduction :FFT
4 points
Splitter
4-point
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 18: Introduction :FFT
8 points
Splitter
4-point
4-point

## Slide 19: Introduction :FFT
8 points
Splitter
4 points
4 points
Splitter
2 points
2 points
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 20: Introduction :FFT
8 points
4 points
4 points
Splitter
2 points
2 points
Splitter
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 21: Introduction :FFT
8 points
Splitter
Splitter
Splitter
2 points
2 points
2 points
2 points
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 22: Introduction :FFT
Complexity calculation :
Because we are continuously dividing by 2, we can determine the exact number of operations based on two factors:
Number of Stages: Since we divide the sequence in half at each step until we reach 2 points
the total number of stages is equal to
  multiplication per Stage: In every stage, we do
The Final Complexity Formulas :
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 23: Introduction :Direct computation vs FFT
Code Flow
Generate bits
Call FFT
Call DFT
Comparing the performance
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 24: Introduction :Direct computation vs FFT
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 25: Introduction :Direct computation vs FFT
Execution Time
4096 point
32768 point
16384 point
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 26: Introduction :Radix-2 vs Radix-4
Number of stages:
Radix-2:
Radix-4:
So, Radix-4 has fewer stages, but does that mean it is better?
Software Perspective: The real bottleneck is memory access. The savings come from reducing the number of times the processor has to write intermediate data to the RAM and read it back again. By cutting the stages from log2​(N) down to log4​(N), Radix-4 cuts the most expensive operation in software (cache/RAM access) exactly in half.
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 27: Introduction :Radix-2 vs Radix-4
Hardware perspective :
The real bottleneck is the stage component
In a pipelined FFT architecture, Radix-2 outperforms Radix-4 in maximum frequency because it has a simpler critical path
  DFT Definition
  DFT calculation methods
  FFT
  Direct computation vs FFT
  Radix-2 vs Radix-4

## Slide 28: Agenda
System definition
Modeling
RTL
Firmware
HW/SW Co-design

## Slide 29: Modeling

## Slide 30: Agenda
Modeling
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 31: Modeling :System Modeling
Mapper
N-point IFFT
Adding cyclic extension
Input data
To the channel
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
Equalizer
De-mapper
De-mapper
Multiplexer
from the channel
from the channel
Output data
Tx (UE)
Rx (Base Station)
  Challenges
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 32: Modeling :Algorithm and Architecture
Algorithm: we implemented the Cooley-Tukey algorithm (Radix-2, DIF)
Architecture :we implemented the SDF architecture (Radix-2, DIF)
Why SDF ?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 33: Recall: Rx block diagram
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
N-point FFT
Removing cyclic extension
Equalizer
De-mapper
De-mapper
De-mapper
Multiplexer
from the channel
from the channel
from the channel
Output data
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 34: FFT Modeling :Algorithm and Architecture
Algorithm: we implemented the Cooley-Tukey algorithm (Radix-2, DIF)
Architecture :we implemented the SDF architecture (Radix-2, DIF)
Why SDF ?
Pros:
Area Efficiency.
Area scaling
Cons:
higher latency (N-1)
low throughput (1 sample/cycle)
High power density
Given the high number of parallel streams in the base station, we prioritized minimizing the area per block over maximizing the single-stream throughput.
But would it really be enough for the required data rate ?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 35: Recall: System Configuration
signal BW, sampling rate
Bandwidth (MHz) | NFFT | NusedFFT (Subcarriers) | NumRBs | Sampling Rate (MHz)
50 | 512 | 384 | 32 | 61.44
100 | 1024 | 792 | 66 | 122.88
400 | 4096 | 3168 | 264 | 491.52
Note: these calculation based on Subcarrier Spacing (SCS): 120 kHz
Would it support 491.52 MHz?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 36: FFT Modeling :Algorithm and Architecture
Platform constraints: "Baseline Frequency: 500 MHz (Validated by a silicon-proven 40nm tape-out)." [1]
Critical Path
So , What is the for the target technology?
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 37: Recall :Adflow Metrics Summary for 3 stages
Metric | Value
Maximum clock frequency | 619.5 MHz
WNS (setup) | 3.386 ns
TNS (setup) | 0
WNS (hold) | 0
TNS (hold) | 0
Post-route utilization | 59.7 %
Technology | GF 22nm
Standard Cell Library | 22nm_gf_fdx_10m
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 38: Modeling:SDF Block Diagram
SDF DIF radix-2
12 bits input
S1
S2
S12
12 bits output
2
2
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 39: Modeling: Fixed point analysis
Q1.11
Q3.9
Q4.8
Q4.8
Q5.7
Q6.6
Q6.6
Q7.5
Q7.5
Q8.4
Q8.4
Q9.3
Q9.3
Stage1
Stage2
Stage3
Stage4
Stage5
Stage6
Stage7
Stage8
Stage9
Stage10
Stage11
Stage12
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 40: Modeling: Fixed point analysis
Q1.11
Q3.9
Q4.8
Q4.8
Q5.7
Q6.6
Q6.6
Q7.5
Q7.5
Q8.4
Q8.4
Q9.3
Q9.3
Stage1
Stage2
Stage3
Stage4
Stage5
Stage6
Stage7
Stage8
Stage9
Stage10
Stage11
Stage12
Chart: Fixed Point Analysis
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Expected expansion | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | -1
MATLAB FxPt | 9 | 8 | 8 | 7 | 6 | 6 | 5 | 5 | 4 | 4 | 3 | 3
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 41: Modeling : SQNR analysis
Example FFT Output Comparison:
Bin | Reference | Fixed point | Error (Magnitude)
1 | −25.92 −16.64i | −25.75 −16.50i | 0.2202
2 | −42.93 −59.19i | −43.00 −59.25i | 0.0922
3 | 8.23 −31.22i | 8.25 −31.13i | 0.0922
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 42: Modeling : SQNR analysis
 | FlPt | FxPt
SQNR |  | 
Mean Error |  | 
Average SQNR = 227.02 dB
Average SQNR = 48.35 dB
Avg Mean error : 1.59 ×
Avg Mean error: 2.417 ×
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 43: Modeling : Challenges
SQNR optimization
Recall : General block diagram
SDF DIF radix-2
n bits input
S1
S2
S12
m bits output
2
2
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 44: Modeling : Challenges
SDF DIF radix-2
12 bits input
S1
S2
S12
12 bits output
2
2
Approach (1) : Truncation
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 45: Modeling : Challenges
Level 1 (Floor rounding – No delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
Could we do better ?
41.25 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 46: Modeling : Challenges
Level 2 (Floor rounding – No delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Recall :
Output equations :
b
Datapath Optimization: Delaying truncation until after the twiddle factor multiplication to improve SQNR
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 47: Modeling : Challenges
Level 2 (Floor rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
Small change , but can we take the SQNR to the next level ?
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 48: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
RoundingMethod:
OverflowAction:
1-Saturate
2-Wrap
Fimath (Fixed-point Mathematic object)
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
1-Floor
2-Celling
3-Zero
4-Nearest
5-Round
6-Convergent

## Slide 49: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
RoundingMethod:
Fimath (Fixed-point Mathematic object)
0.75 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges
1-Floor
2-Celling
3-Zero
4-Nearest
5-Round
6-Convergent
Advantages:
Eliminates rounding bias
Prevents error accumulation across stages
Improves SQNR performance
Matches RTL hardware implementation
Industry standard in DSP hardware

## Slide 50: Modeling : Challenges
Level 3 (Convergent rounding – delayed quantization )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
Level 3
Convergent rounding
delayed quantization
Bit truncation
48.35 dB
0.75 dB
6.45 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 51: Modeling : Challenges
SDF DIF radix-2
12 bits input
S1
S2
S12
20 bits output
2
2
Approach (2) : Bit growth
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 52: Modeling : Challenges
Level 4 (Convergent rounding – delayed quantization - Bit growth )
Level 1
Floor rounding
No delayed quantization
Bit truncation
41.25 dB
Level 2
Floor rounding
delayed quantization
Bit truncation
41.9 dB
Level 3
Convergent rounding
delayed quantization
Bit truncation
48.35 dB
Level 4
Convergent rounding
delayed quantization
Bit growth
58 dB
Area vs SQNR trade-off
9.65 dB
  System Modeling
  Algorithm and Architecture
  SDF Block diagram
  Fixed point analysis
  SQNR analysis
  Challenges

## Slide 53: Agenda
System definition
Modeling
RTL
Firmware
HW/SW Co-design

## Slide 54: RTL

## Slide 55: Agenda
RTL
  SDF Block diagram
  Stage Block diagram
  Stage main component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 56: RTL : stage block diagram
Let's focus on the architecture of a single stage
SDF DIF radix-2
12 bits input
R2
R2
R2
12 bits output
2
2
SDF DIF radix-2
12 bits input
R2
R2
R2
12 bits output
2
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 57: RTL : stage block diagram
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
Output equations :
b

## Slide 58: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
1- Butterfly Function: the core of the stage it does both addition and subtraction, and, in some implementation, it contains also the multiplier block
2- Multiplier Function: Multiplication the output difference from the Butterfly unit

## Slide 59: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
3- Output multiplexer Function: It is used to route the difference (output of the FIFO) and summation to the output (the next stage)
4- Bypass multiplexer Function: It is used to Bypass the summation without multiplying it by the twiddle factors
5- Twiddle factor ROM Function: It holds the values of twiddle factors
0
1
Mux
Twiddle factor ROM

## Slide 60: RTL : stage main component
12 bits input
2
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
FIFO
Twiddle factor ROM
6- FIFO: Function: It’s used to store the input and the difference from the Butterfly unit
7- FIFO multiplexer Function: It’s used to route the input and the output difference to the FIFO
12 bits input
2
0
1
Mux

## Slide 61: RTL: FSM
For demonstration purposes, we will use an 8-point FFT (N=8) , while each stage has its own FSM we will work on stage (1) so the size of FIFO=N/2=4
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
12 bits input
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 62: RTL: FSM
The first state is the IDLE state. The system remains inactive until the wake-up signal
(valid_in) is asserted. This signal is generated by external logic
alongside the input data this is for stage (1) but for the other stages it comes
From the (valid_out) of the previous stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x0
x1
x2
x3
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 63: RTL: FSM
After waking up, the finite state machine (FSM) transitions to the Fill state.
As the name implies, during this state,
the first half of the input samples are loaded into the FIFO.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
12 bits output
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x0
x1
x2
x3
x4
x5
x6
x7
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 64: RTL: FSM
In the Butterfly state, the second half of the input arrives and bypasses the FIFO. Instead, it is processed directly with the first half that we stored earlier. Regarding the outputs of the Butterfly unit: the sum goes directly to the next stage through the output MUX, while the difference is loaded back into the FIFO for the next cycle It is also important to note that once the first output is available, the valid_out signal is asserted to notify the subsequent stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
valid_out
x0
x1
x2
x3
x4
x5
x6
x7
S0
D0
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 65: RTL: FSM
In the Butterfly state, the second half of the input arrives and bypasses the FIFO. Instead, it is processed directly with the first half that we stored earlier. Regarding the outputs of the Butterfly unit: the sum goes directly to the next stage through the output MUX, while the difference is loaded back into the FIFO for the next cycle It is also important to note that once the first output is available, the valid_out signal is asserted to notify the subsequent stage
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
D0 D1 D2 D3
2
S0
S1
S2
S3
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
x7 x6 x5 x4
x3 x2 x1 x0
valid_out
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 66: RTL: FSM
Finally, we reach the Drain state. Here, we perform two operations concurrently. The stored difference data is multiplied by the appropriate twiddle factor and then routed to the next stage. Simultaneously, we load the incoming data for the next frame directly into the FIFO to keep the pipeline completely full.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
valid_out
D3
D2
D1
D0
x0
x1
x2
x3
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 67: RTL: FSM
Finally, we reach the Drain state. Here, we perform two operations concurrently. The stored difference data is multiplied by the appropriate twiddle factor and then routed to the next stage. Simultaneously, we load the incoming data for the next frame directly into the FIFO to keep the pipeline completely full.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
x0 x1 x2 x3
2
D0
D1
D2
D3
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
valid_in
D0 D1 D2 D3
valid_out
x4
x5
x6
x7
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 68: RTL: FSM
From this point, the FSM simply alternates between the Butterfly and Drain states to continuously process the incoming data. This loop continues as long as data is flowing. Once the valid_in signal is De-asserted , meaning we have reached the end of the packet , the FSM transitions back to the IDLE state, ready for the next frame.
BF_S
DRAIN_S
FILL_S
BF_S
IDLE_S
!valid_in
Valid_in
count_done
!count_done
count_done
!count_done
!count_done
count_done && valid_in
count_done && !valid_in
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 69: RTL: Simulation results and latency calculation
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 70: RTL: Challenges
Rounding vs truncation (flooring )
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 71: RTL: Challenges
Different Q notation form sum and multiplier
2
2
Butterfly
0
0
1
1
Mux
Mux
0
1
Mux
Twiddle factor ROM
FIFO
Q2.10
Q2.10
Q3.9
Q3.9
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture

## Slide 72: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Bit reversal :
Recall :
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(4)
X(2)
X(6)
X(1)
X(5)
X(3)
X(7)
Scrambled Output
8-point FFT
x(0)
x(1)
x(2)
x(3)
x(4)
x(5)
x(6)
x(7)
X(0)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ordered Output

## Slide 73: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(4)

## Slide 74: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
Ordered Output
X^(0)
X^(4)

## Slide 75: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
X(0)
Memory (A)
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
X(7)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
Ordered Output
X^(0)
Memory (B)
X^(4)

## Slide 76: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
Memory (A)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
4-Switch the roles: Now Memory A receives the data while Memory B outputs it
Ordered Output
Memory (B)
X^(4)
X^(1)
X^(2)
X^(3)
X^(5)
X^(6)
X^(6)
X^(0)

## Slide 77: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
8-point FFT
SDF - DIF
x(n)
Scrambled Output
Memory (A)
Ping-Pong memory architecture
1-Write in Memory A (7 Clock cycles) Latency
2-Fill in Memory after (15 Clock cycles) Latency
3-Add another Memory (B) to receive the second frame
4-Switch the roles: Now Memory A receives the data while Memory B outputs it
X^(0)
Memory (B)
X^(4)
X^(1)
X^(2)
X^(3)
X^(5)
X^(6)
X^(6)
Ordered Output

## Slide 78: RTL: Challenges
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
Bit reversal :
Problems :
Increasing the area (12.5 KB RAM )
Reducing the max frequency
Increasing the latency form (N-1 ) to (2N-1)
Increasing the power consumption

## Slide 79: RTL: Final Architecture
  SDF Block diagram
  Stage Block Diagram
  Stage Main Component
  FSM
  Simulation results
  Challenges
  Final Architecture
fft4096_dif
in_r
in_i
out_r
out_i
valid_out
Frame_done
out_index
valid_in
rst_n
clk
Singal Name | Function
in_r (input ) , in_r (input) | Input real and input imaginary
valid_in | Enable for the FFT block
valid_out | Asserted when there is a valid output
out_r , out_i | output real and output imaginary
Frame done | Asserted when a frame ends ( for one pulse only )
out_index | The index of the current output
parameter (DATA_WIDTH) | The width of data input and output ports
parameter (ORDERED_OUTPUT) | (1) Ordered output , (0) Scrambled output

## Slide 80: Agenda
System definition
Modeling
RTL
Firmware
HW/SW Co-design

## Slide 81: Firmware

## Slide 82: Agenda
Firmware
  Prerequisites
  Execution Flow
  Single vs. Parallel Performance
  Custom Radix-2 FFT Implementation
  Next Steps

## Slide 83: Firmware: Prerequisites
Installing the pulp-sdk as pulp-dsp depends on it
Pulling the pulp-dsp repository
For large N (N=4096 and above) we need to increase the L1 TCDM size

## Slide 84: Agenda
Firmware
  Prerequisites
  Execution Flow
  Single vs. Parallel Performance
  Custom Radix-2 FFT Implementation
  Next Steps

## Slide 85: Firmware: Execution flow
The FC core wakes up, initializes the data array in L2 Memory, packages a task pointer, and offloads it to the cluster.
Cluster Core 0 wakes up, reads the task, and allocates L1 memory. Core 0 programs the DMA to pull the data from L2 to L1.
Core 0 configures the hardware performance counters and forks Cores 1 through 7, which wake up, divide the butterfly loops, and synchronize execution using barriers. Once finished, the data is DMA-copied back to L2.

## Slide 86: Agenda
Firmware
  Prerequisites
  Execution Flow
  Single vs. Parallel Performance
  Custom Radix-2 FFT Implementation
  Next Steps

## Slide 87: Firmware: Single vs Parallel Performance
Results
Single core | Multi-core

## Slide 88: Firmware: Single vs Parallel Performance
Observations
The input was an impulse in time, and the output is a constant complex amplitude (1 + 0j) across all frequency bin as expected.
The functional correctness of the pulp-dsp functions was considered implicitly validated by design. Because these implementations are sourced directly from the pulp-dsp library, they served as the known-good reference models for our custom radix-2 function development.
The theoretical 8x speedup is not reached due to unavoidable sequential execution overhead (DMA setup and core dispatching), idle clock cycles during hardware barrier synchronization, and memory bank contention when multiple cores access data simultaneously.

## Slide 89: Agenda
Firmware
  Prerequisites
  Execution Flow
  Single vs. Parallel Performance
  Custom Radix-2 FFT Implementation
  Next Steps

## Slide 90: Firmware: Custom Radix-2 FFT Implementation
Took pulp-dsp functions, wrapper structures and naming conventions as a reference, also used some of the helper functions such as bit reversal .
Initially built Radix-2 algorithm using standard C math to verify functionality.
upgraded the scalar standard C math to utilize custom RISC-V vector extension. Using __PACK2, __ADD2, __DOTP2, etc...
Measured the performance of the whole function then the performance of the butterfly

## Slide 91: Firmware: Custom Radix-2 FFT Implementation
Results
Radix-2 FFT (N=4096) | Butterfly
Before running it on multiple cores and using vector operations, It was 1 Million Cycles approx. | Operations being measured:
Radix-2 FFT (N=4096) | Butterfly
Before running it on multiple cores and using vector operations, It was 1 Million Cycles approx. | 

## Slide 92: Agenda
Firmware
  Prerequisites
  Execution Flow
  Single vs. Parallel Performance
  Custom Radix-2 FFT Implementation
  Next Steps

## Slide 93: Firmware: Next steps
System Model Integration: Lock down the exact Q-notation and input bit-width (e.g., 12-bit ADC inputs)
Verification: Comprehensive validation of the C-level fixed point function against MATLAB model made by Fathy
Hardware Accelerator Integration: Replace the C-code butterfly with dedicated hardware made by Darwish

## Slide 94: Agenda
System definition
Modeling
RTL
Firmware
HW/SW Co-design

## Slide 95: HW/SW Co-design

## Slide 96: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 97: HW/SW Co-design : Problem Statement
Objective:
  Integrate a custom-designed Radix-2 FFT Butterfly hardware accelerator into the PULP platform as an AXI peripheral and drive it with a complete software FFT implementation.
Goal:
  Validate correct hardware/software interaction and achieve demonstrable acceleration over a pure software baseline.
Scope of current work:
  Hardware Scope: RTL of radix-2 Butterfly, Map the standalone butterfly accelerator to the AXI bus, design the protocol translation wrapper, and a simple Software validation using a simple C test.
  Software Scope: Develop the bare-metal C drivers, orchestrate the precise movement of 4096 complex points, and restructure the main FFT loop to invoke the hardware.
Current Achievement: T
  The accelerator is now fully integrated and actively invoked by the complete FFT software application, verifying our end-to-end HW/SW co-design

## Slide 98: HW/SW Co-design : PULP SoC – Architecture
No Hidden Caches (The TCDM):
  Normal processors rely on invisible memory caches, which cause unpredictable delays if data is missing.
  PULP replaces caches with a Tightly Coupled Data Memory (TCDM)—a shared, ultra-fast scratchpad where Software must explicitly place data into the TCDM.
The System Actors:
  The Manager (Fabric Controller): The main RISC-V processor that runs our C code and delegates tasks.
  The Delivery Service (Micro-DMA): Autonomously moves raw data from the outside world into the TCDM.
  The Heavy Machinery (Accelerators): Custom hardware that waits for data and a trigger command to perform massive calculations.

## Slide 99: HW/SW Co-design :Highway System – Interconnects and Arbitration
Two Separate Traffic Networks:
  The Fast Lane (TCDM Interconnect): Strictly reserved for instant, 1-cycle memory lookups.
  The Variable-Delay Highway (AXI Crossbar): Built for complex components. Uses a handshaking protocol to safely pause traffic while our FFT crunches math.
How Software Talks to Hardware:
  Address-Based Routing: Hardware doesn't have a name, only a memory address. We mapped our accelerator to.
  The Control Path (Memory-Mapped Registers): The RISC-V manager configures the hardware and sends commands by writing configuration values directly to these addresses.
  The Data Path: Pushing the actual heavy payloads (our complex operands) to the hardware so it can begin computation.
Acc.

## Slide 100: HW/SW Co-design : The Translation Boundary
The Problem: AXI is Too Complex
  Our custom FFT hardware is a raw mathematical engine. It doesn't know how to speak the complex AXI handshaking protocol.
The Blueprint (The .hjson file)
  We define a "contract" between software and hardware using a simple text file
  .hjson, specifying exactly where our operands and triggers live in memory.
The Protocol Downgrade :
  AXI  REG_BUS: A converter strips away AXI routing overhead, leaving only a simple interface (Address, Data, and Write-Enable).
  REG_BUS  Structs: SystemVerilog interfaces cannot plug into auto-generated registers. The bus signals are packed into strict C-like data Structs
The Hardware Reality (.q , .qe, .d, .de) :
  The auto-generated register file unpacks those Structs into raw electrical wires:
    .q : Stable Data, .qe: The Spark (1-cycle trigger pulse)
    .d : The Results from the hardware. (Data), .de : Data Enable.

## Slide 101: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 102: HW/SW Co-design : Butterfly Operation
Core Function:
  The accelerator executes the Radix-2 Decimation-in-Frequency (DIF) butterfly, the fundamental arithmetic building block of the FFT algorithm.
Mathematical Formulation:
Where: L,R : Complex input samples , W : Twiddle factor
Functional Role in FFT:
  Combines input samples
  Applies twiddle rotation
  Produces intermediate FFT outputs
Hardware Role:
  By offloading this highly repetitive equation to custom silicon, we relieve the processor from complex arithmetic computations.

## Slide 103: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 104: HW/SW Co-design : RTL Design
Core blocks:
  Parameterized architecture: IWIDTH, OWIDTH,CWIDTH, SHIFT
  Add/Subtract Units
  Karatsuba Multiplier
  Pipeline / Delay Alignment
Supporting Modules Originally:
  bimpy
    Base signed multiplier
  Longbimpy
    Extended precision multiplier
    Supports larger operand widths
  convround
    Convergent rounding
Currently Used
  standard multiplication logic

## Slide 105: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 106: HW/SW Co-design : Arithmetic Optimization
The Hardware Challenge:
  Complex multiplication is the most expensive operation in our entire Datapath. A standard complex multiply requires 4 real multipliers.
The Optimization Applied: Karatsuba Algorithm
  Reformulated the multiplication logic using the Karatsuba approach. By calculating intermediate products, we complete the math using only 3 real multipliers.
Benefits:
  Reduced multiplier count
  Lower hardware area
  Reduced DSP/resource usage
The Price:
  This approach requires adding extra Adders and Subtractors.

## Slide 107: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 108: HW/SW Co-design : Pipeline Alignment
Motivation:
  Multiplier introduces computation latency
  Addition/Subtraction paths are faster
  Outputs must remain time-aligned
Implemented Solution:
  Auxiliary Signal Propagation:
    i_aux signal tracks valid computation
    Propagated through auxiliary pipeline
    Generates o_aux signal at completion
Result:
  The faster mathematical paths are safely delayed to match the slower paths, ensuring the Sum and Difference outputs arrive perfectly aligned.
  The shift register generates the o_aux signal to correctly indicate pipeline completion.

## Slide 109: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 110: HW/SW Co-design : PULP Integration
Objective:
  Expose the butterfly accelerator as a memory-mapped AXI peripheral within the PULP SoC.
The Integration Components:
  The Blueprint: Defining the hardware/software contract via a Register Map
  The Translator: Using the reggen tool to generate the physical Register File.
  The AXI Wrapper: Encapsulating the auto-generated registers and custom RTL into a single AXI-compliant module.
SoC-Level Modifications :
  Instantiated the top-level wrapper inside the SoC.
  Added a dedicated AXI slave port and extended the interconnect.
  Updated the global address map and inserted the precise AXI decoding rule for routing.

## Slide 111: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 112: HW/SW Co-design : Wrapper Architecture
Purpose:
  Integrates the butterfly accelerator into the PULP AXI-based SoC
  Translates bus transactions into register-level control
Dataflow Overview:
  PULP Processor
  AXI Transactions
  AXI-to-Register Converter
  Register File
  Butterfly Accelerator
Autogenerated Register File Stores: Operands, Twiddle Factors, Control signals and Status/Results
AXI-to-Register Converter:
  Catches memory-mapped AXI transactions from the processor and downgrades them into a generic REG_BUS protocol.
Register <--> Accelerator Interface
  reg_file_to_ip → Configuration & inputs
  ip_to_reg_file → Results & status

## Slide 113: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 114: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 115: HW/SW Co-design : Soc Modifications
Key Modifications:
  Instantiated the top-level wrapper directly inside the pulp_soc.sv source code.
  Added a dedicated AXI slave port to the existing system crossbar.
  Extended the AXI interconnect routing logic to accommodate the new peripheral.
  Updated the global SoC address map to recognize the accelerator.
Address Allocation:
  Assigned a dedicated memory-mapped region for the Butterfly IP.
  This directly enables the RISC-V processor to control the hardware using standard C- load/store instructions (pointers).
Result:
  The custom accelerator is now a fully visible, permanently integrated node on the system bus. It is accessible through standard AXI memory transactions.

## Slide 116: HW/SW Co-design : Software & Verification (1)
Step 1: Verify Mathematical Correctness
  Results Match the results from the Written Testbench
Software Control:
  Simple Custom C test application developed
  Driver functions used for:
    Writing operands
    Configuring coefficients
    Triggering execution
    Polling status
    Reading results
Execution Flow:
  Write inputs to registers
  Trigger accelerator
  Poll DONE status
  Read computed outputs
Observed Results:
  Correct butterfly arithmetic
  Proper trigger (i_aux) and completion signaling (o_aux)
  Successful HW/SW communication

## Slide 117: HW/SW Co-design : Optimization 1 – The Auto-Trigger
The Traditional Approach (3 Bus Transactions):
  Software writes the Left Operand.
  Software writes the Right Operand.
  Software writes a '1' to a dedicated "Start/Control" register to wake up the hardware.
Optimized Solution (2 Bus Transactions):
  Eliminated the dedicated "Start" register.
  Flagged the Right Operand register to generate a Write-Enable pulse.
The Benefit:
  The exact moment the RISC-V processor delivers the final piece of data, the hardware instantly fires up and begins the pipeline. This saves a redundant AXI transaction on every single butterfly calculation.
Result:
  Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 118: HW/SW Co-design : Optimization 2 – Auto-Status
The Polling Problem:
  Software must poll a "Status" register to know when the computation is done.
  Traditionally, software must manually write a '0' to clear this flag before starting a new calculation, wasting another AXI transaction.
Solution (The .de Wire):
  We used the Data Enable (.de) wire to make the hardware self-managing.
  Auto-Clear:
    status.de = w_o_aux | op_right.qe; The exact moment a new trigger fires (op_right.qe), the hardware forces the status bit back to ‘0’.
  Auto-Set:
    When the pipeline finishes (w_o_aux), it drives the status bit to '1’.
Data Latching:
  The output results (result_left, result_right) are strictly gated by .de = w_o_aux. The register file cannot capture garbage data mid-calculation; it only latches the final, mathematically valid answers.
Result:
  Saved another AXI transaction. So,Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 119: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling
  Phase 1: The Unoptimized Baseline
    Architecture: Passing full 32-bit complex Twiddle factors from SW.
    Using pipelined longbimpy multiplier IPs.
    No wrapper optimizations.
    Hardware Latency: 14-16 cycles, Total Software Latency (Round-Trip): 442 cycles per butterfly.
  Phase 2: Initial Tuning
    Architecture: Basic software driver overhead minimized.
    Still passing full Twiddle factors over AXI and utilizing longbimpy
    .Hardware Latency: 14-16 cycles , Total Software Latency: Reduced to 59 cycles.
  Phase 3: The Final Optimized Architecture
    Architecture: Swapped to standard combinational multipliers.
    Replaced AXI Twiddle payload with a simple Twiddle Index to leverage internal ROM.
    Auto-Trigger & Auto-Status.
    Hardware Latency: 7 cycles, Total Software Latency: 24 cycles per butterfly.

## Slide 120: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling
  Phase 2: Result
  Phase 3: Result

## Slide 121: HW/SW Co-design :Questions??
Overhead Sources ?
Pulp-runtime vs SDK, Is there a difference for SW latency and/or total overhead ?
Are the Results Valid and Logical ?

## Slide 122: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 123: HW/SW Co-design : Current Status
Completed:
  Radix-2 butterfly RTL implementation
  AXI wrapper design
  Register interface integration
  SoC-level AXI integration into PULP
Validation Achieved:
  Correct arithmetic functionality
  Successful AXI communication
  Proper register-based control

## Slide 124: Agenda
HW/SW Co-design
  Problem Statement
  Butterfly Operation
  RTL Design
  Arithmetic Optimization
  Pipeline Alignment
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification
  Current Status
  Next Steps

## Slide 125: HW/SW Co-design : Next Steps
Full FFT Software Integration
  Collaborate with Moustafa Youssry to
  Integrate the butterfly accelerator into the complete FFT software flow
RTL & Numerical Consistency
Collaborate with Moustafa Fathy and Marwan Khaled to
Synchronize:
  Fixed-point analysis
  Butterfly arithmetic behavior
  FFT RTL implementation

## Slide 126: GitHub Repositories
1- MATLAB modeling code for SDF DIF : (Modeling part by Mostafa Fathy)
2- SDF 4092-point code : (RTL part by Marwan Khaled and Mostafa Fathy)
3- Source code can be found here: (Firmware part by Mostafa Yossry) https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/Firmware/Radix2-FFT 4- RTL implementations and Wrapper codes can be found here: (AXI integration part by Mostafa Ahmed)
https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/RTL

## Slide 127: References
1- Fast Fourier Transform :Algorithms And Applications)
https://danylastchild07.wordpress.com/wp-content/uploads/2016/05/fft_algorithms-and-applications.pdf
2- VLSI Digital Signal Processing Systems: Design and Implementation
https://d1.amobbs.com/bbs_upload782111/files_18/ourdev_480582.pdf
3- PULP platform
https://pulp-platform.org/index.html

## Slide 128
Thank You!