## Slide 1
Front end team …..
ADI/CU GP 2025/2026
Progress Update Meeting (2)

## Slide 2: Agenda
HW/SW Co-design (HW Part)
HW/SW Co-design (SW Part)
Multi clusters
HWPE

## Slide 3: HW/SW Co-design (HW Part)

## Slide 4: Agenda
HW/SW Co-design
  Where we were?
  AXI butterfly Latency analysis
  Moving to TCDM
  PULP Integration
  Wrapper Architecture
  SoC Modifications
  Software & Verification (1)
  Optimizations
  Software & Verification (2)

## Slide 5: HW/SW Co-design : Optimization 1 – The Auto-Trigger
The Traditional Approach (3 Bus Transactions):
  Software writes the Left Operand.
  Software writes the Right Operand.
  Software writes a '1' to a CTRL register to wake up the hardware.
Optimized Solution (2 Bus Transactions):
  Eliminated the dedicated "Start" register.
  Flagged the Right Operand register to generate a Write-Enable pulse.
The Benefit:
  The hardware instantly fires up instantly.
  Saves AXI transaction on every single butterfly
Result:
  Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 6: HW/SW Co-design : Optimization 2 – Auto-Status
The Polling Problem:
  Software must manually clear this STATUS flag before new calculation, wasting an AXI transaction.
Solution (The .de Wire):
  status.d = w_o_aux ? 1'b1 : 1’b0, status.de = w_o_aux | op_right.qe
Result:
  Saved another AXI transaction. So,Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 7: HW/SW Co-design : Where were we?
Latency Profiling
Design Feature | Phase 1 (Pipelined) | Phase 2 (Pipelined) | Phase 3 (Pipelined)
Operand Widths | Oversized: 34b In, 38b Out, 42b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Delivery | Full payload passed over AXI | Full payload passed over AXI | Twiddle Index passed over AXI
Wrapper | No optimizations | No optimizations | optimized
Multiplier Type | Pipelined | Pipelined | Standard
Software Driver | High Overhead | Optimized | Optimized
Latency | 442 cycles | 59 cycles | 24 cycles
Phase 4 (Flattened)
Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Index passed over AXI
optimized
Standard
Optimized
18 cycles

## Slide 8: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : Latency = 7 Write + 2 butterfly + 7 Read = 16 cycles

## Slide 9: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : Write Phase : 7 cycles = 1 twiddle index + 3 left operand + 3 right operand

## Slide 10: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : 3 cycles between writes on bus
Cycle 1: Capture
  aw_valid, w_valid, aw_ready, and w_ready The hardware captures both the destination address and the operand data.
Cycle 2: The Confirmation Response
  The Wrapper asserts b_valid and the CPU asserts b_ready to acknowledge that the data was safely written.
Cycle 3: The State Machine Reset
  The b_valid signal drops. The AXI slave requires a clock cycle to reset its internal state machine before it can accept new data.

## Slide 11: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : 2 cycles for butterfly operation = 1 intermediate values + 1 final results

## Slide 12: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : Read Phase : 7 cycles = 3 left result + 3 right result + 1 cycle gap

## Slide 13: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling :read takes 3 cycles
Cycle 1: The Address Handshake
  The CPU asserts ar_valid to request a specific memory address.
  The Wrapper asserts ar_ready to accept the request.
Cycle 2: Preparing Data
  HW fetches the requested result
Cycle 3: The Data Handshake
  The Wrapper asserts r_valid and pushes the computed math onto the bus.
  The CPU asserts r_ready to capture the returned data.
Gap cycle (The storage Cycle)
  The CPU de-asserts ar_valid and the bus goes completely silent. In order for the CPU to store result in one of its internal registers

## Slide 14: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : Latency = 7 Write + 2 butterfly + 7 Read = 16 cycles

## Slide 15: HW/SW Co-design : Flattened AXI Integrated Butterfly
Latency Profiling : Latency = 7 Write + 2 butterfly + 7 Read = 16 cycles
APIs used to calculate latency perf_start and perf_stop, each takes a cycle
Therefore 16 cycles + 2 cycles = 18 cycles

## Slide 16: HW/SW Co-design : Moving to TCDM
Objective:
  Re-integrate the custom-designed Radix-2 FFT Butterfly hardware accelerator directly into the PULP platform's TCDM (Tightly Coupled Data Memory) interconnect to eliminate AXI bus overhead.
Goal:
  Achieve physical-limit execution latency
Scope of current work:
  Hardware Scope:
    Map the butterfly accelerator to the TCDM busand design a low-latency protocol translation wrapper

## Slide 17: HW/SW Co-design : PULP Intergation
Objective:
  Expose the butterfly accelerator as a memory-mapped AXI peripheral within the PULP SoC.
Pulp Architecture Overview
The TCDM:
  Normal processors rely on invisible memory caches, which cause unpredictable delays.
  PULP replaces caches with a Tightly Coupled Data Memory (TCDM)—a shared, ultra-fast scratchpad where Software must explicitly place data into the TCDM.
The System Actors:
    Fabric Controller
    Micro-DMA
    Accelerators

## Slide 18: HW/SW Co-design :Highway System – Interconnects and Arbitration
Two Separate Traffic Networks:
  TCDM Interconnect: reserved for fast operations, 1-cycle memory lookups.
  AXI Crossbar: Built for complex components that needs multiple cycles.
How Software Talks to Hardware:
  Address-Based Routing: Hardware doesn't have a name, only a memory address.
Two Paths of Communication:
  The Control Path :The FC configures the hardware by writing values to these addresses.
  The Data Path: Pushing the heavy payloads to the hardware so it can begin computation.
Wrapper
Accelerator

## Slide 19: HW/SW Co-design : The Translation Wrapper
The Problem: AXI Overhead
  The multi-channel AXI handshake crippled our math core, turning a 2-cycle computation into a 18-cycle bottleneck.
Solution: TCDM Integration
  The Blueprint (The .hjson file)
  A "contract" between software and hardware.
The Protocol Downgrade :
  TCDM  Direct Protocol Converter  REG_BUS
  REG_BUS  Macros  Structs
The Hardware Reality (.q , .qe, .d, .de) :
  .q & .qe: Stable inputs and the 1-cycle Auto-Trigger spark.
  Safety Latches to .d: TCDM has one cycle delay to read so we latch results steady for an extra cycle

## Slide 20: HW/SW Co-design : Soc Modifications (TCDM )
Key Modifications:
  Instantiated the top-level TCDM wrapper inside the pulp_soc.sv top module.
  Declared a dedicated XBAR_TCDM_BUS interface to physically wire the accelerator into the system.
  Updated L2 Demux Routing: Expanded NR_RULES_L2_DEMUX and added an addressing rule to funnel the Butterfly's memory space from the main cluster into the Contiguous Crossbar.
  Updated Crossbar Routing: Expanded NR_RULES_CONTIG_CROSSBAR and mapped the incoming traffic directly to the newly instantiated TCDM slave port.
Address Allocation:
  Assigned a dedicated memory-mapped region (0x1C01_0000 to 0x1C09_0000) inside soc_mem_map.svh.
Result:
  The custom accelerator is now a fully visible, permanently integrated node directly on the Tightly Coupled Data Memory (TCDM) highway. It is accessible through ultra-fast, 1-cycle memory transactions, completely bypassing the AXI crossbar.

## Slide 21: HW/SW Co-design : Software & Verification (1)
Step 1: Verify Integration &Mathematical Correctness
  Results Match the results from the Written Testbench
Software Control:
  Simple Custom C test application developed
Execution Flow:
  Write inputs to registers
  Trigger accelerator
  Poll DONE status
  Read computed outputs
Observed Results:
  Correct butterfly arithmetic
  Successful HW/SW communication
Measured Latency At first was 48 cycles, But we reached 18 cycles with AXI

## Slide 22: HW/SW Co-design : Optimization 1 – The Auto-Trigger
The Traditional Approach (3 Bus Transactions):
  Software writes the Left Operand.
  Software writes the Right Operand.
  Software writes a '1' to a CTRL register to wake up the hardware.
Optimized Solution (2 Bus Transactions):
  Eliminated the dedicated "Start" register.
  Flagged the Right Operand register to generate a Write-Enable pulse.
The Benefit:
  The hardware instantly fires up instantly.
  Saves a transaction on every single butterfly
Result:
  Number of Cycles taken for the End-to-end Butterfly execution decreased.

## Slide 23: HW/SW Co-design : Where we were?
Latency Profiling
Design Feature | Phase 1 (AXI Pipelined) | Phase 2 (AXI Pipelined) | Phase 3 (AXI Pipelined) | Phase 4 (AXI Flattened)
Operand Widths | Oversized: 34b In, 38b Out, 42b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle | Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Delivery | Full payload passed over AXI | Full payload passed over AXI | Twiddle Index passed over AXI | Twiddle Index passed over AXI
Wrapper | No optimizations | No optimizations | optimized | optimized
Multiplier Type | Pipelined | Pipelined | Standard | Standard
Software Driver | High Overhead | Optimized | First Optimized | Fully Optimized
Latency | 442 cycles | 59 cycles | 24 cycles | 18 cycles
Phase 5 (TCDM Flattened)
Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Index passed
No optimizations
Standard
High Overhead
48 cycles
Phase 6 (TCDM Flattened)
Corrected: 24b In, 24b Out, 32b Twiddle
Twiddle Index passed
optimized
Standard
Optimized
11 cycles

## Slide 24: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling : 9 cycles + 2 APIs = 11 cycles

## Slide 25: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling : Writing 3 times takes 3 cycles

## Slide 26: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling : 2 cycles butterfly + 1 delay to match TCDM  Question

## Slide 27: HW/SW Co-design : Software & Verification (2)
Step 2:Latency Profiling : 3 cycles read results and addresses

## Slide 28
Thank You!