## Slide 1
Moustafa Ahmed
Radix-2 FFT Butterfly Hardware Accelerator Integration into PULP
ADI/CU GP 2025/2026

## Slide 2: HW/SW Co-design : PULP SoC – Architecture
No Hidden Caches (The TCDM):
  Normal processors rely on invisible memory caches, which cause unpredictable delays if data is missing.
  PULP replaces caches with a Tightly Coupled Data Memory (TCDM)—a shared, ultra-fast scratchpad where Software must explicitly place data into the TCDM.
The System Actors (The "Factory Floor"):
  The Manager (Fabric Controller): The main RISC-V processor that runs our C code and delegates tasks.
  The Delivery Service (Micro-DMA): Autonomously moves raw data from the outside world into the TCDM.
  The Heavy Machinery (Accelerators): Custom hardware that waits for data and a trigger command to perform massive calculations.

## Slide 3: HW/SW Co-design :Highway System – Interconnects and Arbitration
Two Separate Traffic Networks:
  The Fast Lane (TCDM Interconnect): Strictly reserved for instant, 1-cycle memory lookups.
  The Variable-Delay Highway (AXI Crossbar): Built for complex components. Uses a handshaking protocol to safely pause traffic while our FFT crunches math.
How Software Talks to Hardware:
  Address-Based Routing: Hardware doesn't have a name, only a memory address. We mapped our accelerator to.
  The Control Path (Memory-Mapped Registers): The RISC-V manager configures the hardware and sends commands by writing configuration values directly to these addresses.
  The Data Path: Pushing the actual heavy payloads (our complex operands) to the hardware so it can begin computation.
Acc.

## Slide 4: HW/SW Co-design : The Translation Boundary
The Problem: AXI is Too Complex
  Our custom FFT hardware is a raw mathematical engine. It doesn't know how to speak the complex AXI handshaking protocol.
The Blueprint (The .hjson file)
  We define a "contract" between software and hardware using a simple text file
  .hjson, specifying exactly where our operands and triggers live in memory.
The Protocol Downgrade :
  AXI  REG_BUS: A converter strips away AXI routing overhead, leaving only a simple interface (Address, Data, and Write-Enable).
  REG_BUS  Structs: SystemVerilog interfaces cannot plug into auto-generated registers. The bus signals are packed into strict C-like data Structs
The Hardware Reality (.q , .qe, .d, .de) :
  The auto-generated register file unpacks those Structs into raw electrical wires:
    .q : Stable Data, .qe: The Spark (1-cycle trigger pulse)
    .d : The Results from the hardware. (Data), .de : Data Enable.

## Slide 5: Problem Statement
Objective:
  Integrate a custom-designed Radix-2 FFT Butterfly hardware accelerator into the PULP platform
Goal:
  Validate correct hardware/software interaction via: Custom Radix-2 FFT Implementation
Scope of current work:
  Standalone butterfly accelerator integration
  Software validation using a simple C test
Current limitation:
  Accelerator is not yet invoked by a complete FFT software implementation

## Slide 6: Radix-2 Butterfly Operation
The implemented accelerator performs the Radix-2 Decimation-in-Frequency (DIF) butterfly, a fundamental computation stage in FFT algorithms
Mathematical Formulation:
Where: L,R : Complex input samples , W = Twiddle factor
Functional Role in FFT:
  Combines input samples
  Applies twiddle rotation
  Produces intermediate FFT outputs

## Slide 7: Butterfly RTL Architecture
Core blocks:
  Parameterized architecture: IWIDTH, OWIDTH,CWIDTH, SHIFT
  Add/Subtract Units
  Karatsuba Multiplier
  Pipeline / Delay Alignment
Supporting Modules:
  bimpy
    Base signed multiplier
  Longbimpy
    Extended precision multiplier
    Supports larger operand widths
  convround
    Convergent rounding

## Slide 8: Arithmetic Optimization
Challenge: Complex multiplication is the most expensive operation in the butterfly datapath.
  Standard complex multiply requires 4 real multipliers
Optimization Applied: Karatsuba Algorithm
  Reformulates multiplication using:
  3 real multipliers instead of 4
Benefits:
  Reduced multiplier count
  Lower hardware area
  Reduced DSP/resource usage
Price:
  More Adders/Subtractors

## Slide 9: Pipeline and Latency Alignment
Motivation:
  Multiplier introduces computation latency
  Addition/Subtraction paths are faster
  Outputs must remain time-aligned
Implemented Solution:
  Auxiliary Signal Propagation:
    i_aux tracks valid computation
    Propagated through auxiliary pipeline
    Generates o_aux at completion
Result:
  Sum and difference outputs aligned
  Pipeline completion correctly indicated

## Slide 10: Hardware Integration into PULP
Objective:
  Expose the butterfly accelerator as a memory-mapped AXI peripheral within the PULP SoC.
Integration Components:
  Register map definition (HJSON)
  reggen-generated register file
  AXI wrapper
  AXI interconnect extension
SoC-Level Modifications:
  Wrapper instantiated
  AXI slave port added
  Address map updated
  AXI decoding rule inserted

## Slide 11: Wrapper Architecture
Purpose:
  Integrates the butterfly accelerator into the PULP AXI-based SoC
  Translates bus transactions into register-level control
Dataflow Overview:
  PULP Processor
  AXI Transactions
  AXI-to-Register Converter
  Register File
  Butterfly Accelerator
Autogenerated Register File Stores: Operands, Twiddle Factors, Control signals and Status/Results
AXI-to-Register Converter:
  Converts AXI protocol → Generic Register Bus
  Enables memory-mapped register access
Register <--> Accelerator Interface
  reg_file_to_ip → Configuration & inputs
  ip_to_reg_file → Results & status

## Slide 12: SoC-Level Integration into PULP
Key Modifications:
  Wrapper instantiated in pulp_soc.sv
  AXI slave port added
  AXI interconnect extended
  Address map updated
Address Allocation
  Dedicated memory-mapped region assigned
  Enables processor access via load/store
Result
  Accelerator visible to the system bus
  Accessible through AXI transactions

## Slide 13: Software Interaction, Result & Verification
Software Control:
  Simple Custom C test application developed
  Driver functions used for:
    Writing operands
    Configuring coefficients
    Triggering execution
    Polling status
    Reading results
Execution Flow:
  Write inputs to registers
  Trigger accelerator
  Poll DONE status
  Read computed outputs
Observed Results:
  Correct butterfly arithmetic
  Proper trigger (i_aux) and completion signaling (o_aux)
  Successful HW/SW communication

## Slide 14: Current Status
Completed:
  Radix-2 butterfly RTL implementation
  AXI wrapper design
  Register interface integration
  SoC-level AXI integration into PULP
Validation Achieved:
  Correct arithmetic functionality
  Successful AXI communication
  Proper register-based control

## Slide 15: Next Steps
Full FFT Software Integration
  Collaborate with Moustafa Youssry to
  Integrate the butterfly accelerator into the complete FFT software flow
RTL & Numerical Consistency
Collaborate with Moustafa Fathy and Marwan Khaled to
Synchronize:
  Fixed-point analysis
  Butterfly arithmetic behavior
  FFT RTL implementation

## Slide 16: GitHub Repository
RTL implementations and Wrapper codes can be found here:
https://github.com/Mostafa-Yossry/ADI-CU-GP-2025-2026/tree/main/RTL